## Slide 1: RobotC Introductory Seminar: Advanced Topics
Robert Atkinson
Mentor, FTC Team 417
bob@theatkinsons.org
27 August 2011

## Slide 2: Overview
Joysticks
  Taking human control of your bot
Motors
  Making your robot go
Telemetry
  Getting actual data off the NXT so you can understand why on earth it didn’t do what you thought you told it to do
Tasks
  Doing several things at once

## Slide 3: Joystick Controllers
TeleOp mode in First Tech Challege is played with one or two 10-button joystick controllers
Robot/Debugger Windows/Joystick Control - Game

## Slide 4: Joystick Controllers: Basics
#include “JoystickDriver.h”
  Compatible with “JoystickDriver.c” built-in to RobotC
  Includes enhancements and bug fixes
getJoystickSettings(joystick) function
  Reads the current state of the joystick controllers into the global variable ‘joystick’
  Returns a Boolean indicating whether there’s anything new since the last time it was called.
    if (getJoystickSettings(joystick))
    {
    …
    }

## Slide 5: Joystick Controllers: Buttons
Each of the buttons has a name:
  JOYBTN_LEFTTRIGGER_UPPER, JOYBTN_RIGHTTRIGGER_UPPER, JOYBTN_LEFTTRIGGER_LOWER, JOYBTN_RIGHTTRIGGER_LOWER, JOYBTN_TOP_LEFT, JOYBTN_TOP_RIGHT, JOYBTN_JOYSTICK_LEFT, JOYBTN_JOYSTICK_RIGHT, JOYBTN_1, JOYBTN_2, JOYBTN_3, JOYBTN_4
joyBtn(jyc, button) returns true if ‘button’ is pressed on controller ‘jyc’ (which should have value 1 or 2)
  if (joyBtn(jyc, JOYBTN_RIGHTTRIGGER_LOWER))
  {
  …
  }
joyBtnOnce(jyc, button) is like joyBtn(jyc, button), but returns true only once per button press
  In your UI, this is often actually what you want: something to happen exactly once whenever a certain button is pressed

## Slide 6: Joystick Controllers: Hat
The ‘hat’ is sometimes called ‘directional pad’
  But ‘hat’ is shorter and sweeter to type 
Eight different directions:
  JOYHAT_UP, JOYHAT_UPRIGHT, JOYHAT_RIGHT, JOYHAT_DOWNRIGHT, JOYHAT_DOWN, JOYHAT_DOWNLEFT, JOYHAT_LEFT, JOYHAT_UPLEFT, JOYHAT_NONE
joyHat(jyc, hat) returns true if the hat on controller ‘jyc’ is in position ‘hat’
  if (joyHat(jyc, JOYHAT_RIGHT))
  {
  …
  }
joyHatOnce(jyc, hat) like joyHat(jyc, hat), but only returns true once until the hat is no longer in the ‘hat’ position

## Slide 7: Joysticks Controllers: Communication Disconnect
What if communication between your human driver and your bot goes down?
  Rare, but it does happen
  Want to take conservative protective measures (stop the bot!)
joyMessageTime() returns the time at which the last joystick message was received
  Compare against system clock: nSysTime
joyMessageCount() returns how many messages we’ve seen
  Can only ‘lose’ communication if we’ve had some already
  if (joyMessageCount() > 0 && nSysTime - joyMessageTime() > 1000)
  {
  …
  }

## Slide 8: Fun: Making Music and Beeps
#include “music.h”
  int musicFifth[] =
  {
  NOTE_G, NOTE_EIGHTH,
  NOTE_G, NOTE_EIGHTH,
  NOTE_G, NOTE_EIGHTH,
  NOTE_E_FLAT, NOTE_HALF,
  };
  …
  PlayMusic(musicFifth, 100, NOTE_QUARTER);
  …
Making beeps
  …
  Beep();
  Beep(NOTE_D);
  Beep(NOTE_E_FLAT, 300);
  …

## Slide 9: Joystick Controllers: Exercise
Write a program that plays a tune when the left upper trigger of joystick controller #1 is pressed
  Compare the use of joyBtn(jyc,…) with joyBtnOnce(jyc,…)
#include "joystickdriver.h"
#include "music.h"
task main()
{
Beep(); // make a noise when we start
int jyc = 1; // we’ll use controller#1
while (true)
{
if (there’s new joystick data available)
{
respond to the joystick state
}
else if (we’ve been disconnected)
{
do something about it
}
}
}

## Slide 10: Joystick Controllers: Joysticks
Two joysticks, each with X & Y directions
  Each value is in range -128 to 127
  Joysticks don’t return exactly to zero
    Use a ‘dead zone’
joyX(jyc, JOY_LEFT) returns the current value of the left joystick on controller ‘jyc’
  joyX(jyc, JOY_RIGHT), joyY(jyc, JOY_LEFT), joyY(jyc, JOY_RIGHT) similar
    int stickRange = 128 - joyThrottleDeadZone;
    int motorRange = 100;
    int stick = joyY(jyc, JOY_LEFT);
    int motorPower = Max(0, abs(stick) - joyThrottleDeadZone) *
    motorRange / stickRange;
    if (stick < 0)
    motorPower = -motorPower;

## Slide 11: Joystick Controllers: Joysticks (cnt’d)
joyFlick(jyc, JOY_LEFT, JOYDIR_LEFT) returns true if the left joystick of controller ‘jyc’ is flicked to the left
  JOYDIR_LEFT, JOYDIR_RIGHT, JOYDIR_UP, JOYDIR_DOWN
  Sort of allows the use of a joystick like four additional buttons
    if (joyFlick(jyc,JOY_RIGHT,JOY_UP))
    {
    …
    }
joyFlickOnce(jyc, JOY_LEFT, JOYDIR_UP) returns true only once per flick

## Slide 12: Motors
Two kinds of motors
  Plastic Lego motors
  Steel 12V Tetrix motors
In competition we use mostly Tetrix motors
  Power, torque, physical robustness
  But more complicated wiring
We’ll use Lego motors here
  Simplicity
Different electrically, similar programatically

## Slide 13: Motors: Configuration
Configure two Lego motors
  As if for a “tank-drive” robot
  Robot/Motor and Sensors Setup
    Will insert #pragma statements at start of your .c file

## Slide 14: Motors: Control
Set motor power level using motor[] array
    motor[motorLeft] = motorPower;
    motor[motorRight] = motorPower;
Motor power ranges from -100 to +100
  -100 == full reverse,
  100 == full forward,
  0 == stop
  Power values of magnitude > 100 are clamped automatically

## Slide 15: Motors: Encoders
Optical ‘encoders’ attached to motor shafts keep track of how far the shaft turns
  Use: you can know how far your robot goes!
  Encoders built-in to Lego motors
  Optional addition to Tetrix motors
    Use whenever you can
Number of encoder ticks per revolution
  360 for Lego motors
  1440 for Tetrix motors (== 4 * 360)
nMotorEncoder[] array returns encoder values
  nMotorEncoder[motorLeft]

## Slide 16: Debugging: Tracing to Debug Stream
A place where you can write simple tracing output during program development
  Can be really, really handy way to find out what on earth your program is up to
  Robot / Debugger Windows/ Debug Stream
  Robot / Debugger / (Pause Refresh vs. Continuous)
writeDebugStreamLine(“format string”, values)
    writeDebugStreamLine(“my int is: %d”, 3);
    writeDebugStreamLine(“my str is: %s”, “hello”);
    writeDebugStreamLine(“value of pi is: %f”, PI);
    writeDebugStreamLine(“page: %d of %d”, pageNumber, pageCount);
Caution: tracing can be slow-ish
  Keep things to just a few traces per second at most

## Slide 17: Motors: Exercise
Modify your joystick controller exercise to:
  Use the Y value of the left joystick for power
    Forward and backward motion of your bot
  Use the X value of the right joystick for steering
    Left and right motion of your bot
  Every half second trace the encoder values to the debug stream
    Bonus: report # of motor revolutions instead of raw encoder values
Hints:
  Get the forward/backward part fully working before worrying about the left/right part
  Then do the tracing part
    The nSysTime variable gives you the system time in milliseconds

## Slide 18: Motors: Cautions
Some built-in RobotC motor features only work for Lego motors, not Tetrix motors
  nSyncedMotors, nSyncedTurnRatio, nMotorRunState, nMaxRegulatedSpeedNXT
    nMaxRegulatedSpeed12V has no effect, documentation to the contrary notwithstanding
  nMotorEncoderTarget not reliable for 12V
    You can accomplish the same effect yourself though
RobotC initializes Tetrix motors when the NXT brick is powered on
  Thus, ALWAYS power on your NXT brick after your 12V power supply
  Otherwise, motors will coast instead of brake at zero power

## Slide 19: Telemetry
Consider the following:
  Somehow your bot isn’t behaving like you think it should
    Maybe you’re trying to turn the bot using the gyro sensor, and it’s not getting the angle right. Why? Where does the fault lie?
  So you want to get some hard data to see what’s going on
    Maybe lots and lots of data
    And what you really want is some nice charts of this data
RobotC has built in data-logging, but
  Limited in capacity to 5k of data
    In practice, just not enough
  Multiple items per record cumbersome and awkward
  Only integer data supported
  After program is finished, many-click manual steps needed to import into spreadsheet
    Data is staged in files on NXT

## Slide 20: Telemetry: TelemetryFTC
Real-time telemetry streaming from NXT directly into Microsoft Excel
  Up to about 1000 records per second achievable
  Virtually unlimited data capacity
  All basic data types supported
    int8, int16, int32, uint8, uint16, uint32,
    float, string, bool, char
  Programatically easy to create multi-item records
  Easy to use

## Slide 21: Telemetry: TelemetryFTC Basics
Add telemetry calls to your program
  Once:
    TelemetryInitialize();
    TelemetryUseBluetooth(true); // if telemetry will indeed use Bluetooth
  As needed:
    TelemetryAddInt32(nMotorEncoder[motorLeft]);
    TelemetryAddFloat(PI * someFunction());
    TelemetryAddString(“hello”);
    TelemetrySend();
  See TelemetrySample.c for other examples
Run TelemetryFTC
  Connect to your NXT using TelmetryFTC UI
Run your program on your NXT
  Excel sheet will open automatically and fill up with data
  Each telemetry record will be a row in the sheet
  Each item in each record will be in its own column
Caveat
  RobotC and TelemetryFTC can’t both use Bluetooth simultaneously, so
  Connect one with Bluetooth and the other with USB, or
  Disconnect RobotC and run program manually using NXT buttons
    TelemetryFTC can send joystick to NXT

## Slide 22: Telemetry: Excercise
Write a program that sends telemetry records containing the values of the left and right motor encoders
  Run each motor at
    power==100 for 2 seconds, then power==0 for 1 second
    power==90 for 2 seconds, then power==0 for 1 second
    power==80 for 2 seconds, …
    etc
  Include a ms timestamp and a telemetry record serial # as the first two items in each telemetry record
  Include appropriate column headers as a first telemetry record
  Plot the results in an Excel graph
Hint:
  TelemetrySample.c has examples

## Slide 23: Advanced++ Topic: Tasks
“Multitasking” is a term used to describe the act of somone doing many things at the same time
In much the same way, computer programs can run multiple tasks concurrently
This technique is like a sharp knife
  It can do it’s job very effectively
  But it can cut you if you’re not careful
  Keeping yourself safe takes constant vigilance and careful thinking
    This is rocket science

## Slide 24: Tasks: Mechanisms
‘task’ keyword indicates a new task
    task displayTask() { … }
Each task will execute concurrently with other tasks
  Reality: each task executes for a little while, then the next one gets a turn
    Hundreds or thousands of times per second
    Non-deterministic
Functions for manipulating tasks
  StartTask(displayTask)
  StopTask(displayTask)
  EndTimeSlice()
    Current task has nothing better to do
    Let’s other tasks run
Tasks can have priorities
  But there be dragons
  Using task priorities will only give you grief
  Don’t use them! Just don’t!

## Slide 25: Tasks: Pitfalls of Concurrency
void deposit(float depositAmount)
{
float balance = readCurrentBalance(); // 1
balance += depositAmount; // 2
writeCurrentBalance(balance); // 3
}
void withdraw(float withdrawalAmount)
{
float balance = readCurrentBalance(); // 4
balance -= withdrawalAmount; // 5
writeCurrentBalance(balance); // 6
}
task oneTask()
{
...
deposit(100.00);
...
}
task anotherTask()
{
...
withdraw(50.00);
...
}
What happens if oneTask() and anotherTask() execute ‘simultaneously’?
  Execution order: 1,2,3,4,5,6: ok
  Execution order: 4,5,6,1,2,3: ok
  Execution order: 1,4,2,3,5,6: disaster

## Slide 26: Tasks: Locking
#include “Lock.h”
LOCK accountLock;
void deposit(float depositAmount)
{
LockExclusive(accountLock);
//
float balance = readCurrentBalance(); // 1
balance += depositAmount; // 2
writeCurrentBalance(balance); // 3
//
ReleaseLock(accountLock);
}
void withdraw(float withdrawalAmount)
{
LockExclusive(accountLock);
//
float balance = readCurrentBalance(); // 4
balance -= withdrawalAmount; // 5
writeCurrentBalance(balance); // 6
//
ReleaseLock(accountLock);
}
task oneTask()
{
...
deposit(100.00);
...
}
task anotherTask()
{
...
withdraw(50.00);
...
}
task main()
{
InitializeLock(accountLock);
StartTask(oneTask);
StartTask(anotherTask);
}

## Slide 27: Tasks: Three Task Architecture
Main task
  Main app logic
  “Drive 30cm, Turn left 90deg, Drive until you hit a white line”
  Often ‘blocks’, waiting for something to finish or some event to happen
‘Blackboard’ task
  High frequency task
    Maybe 50 ms interval
  Does repetative stuff that needs constant and frequent attention
  Only task to actually read sensor values
    Computes derived sensor values
      E.g.: gyro reports rate of turn, want accumulated turn angle
    Stores values in global variables
    Computes ‘stop condition’ events for each sensor
      E.g.: has the gyro reached a certain angle
      E.g.: does the color sensor see a requested color (white)
    Main task indicates which sensors and stop conditions are of interest
  Does miscellaneous housekeeping
    E.g.: Check for motor stall (this will save you $$$!)
    E.g.: Check for rotational servo stall
    E.g.: Send heartbeat message to hardware that needs it

## Slide 28: Tasks: Three Task Architecure (cnt’d)
Display task
  Low frequency task
    Maybe 750 ms interval
  Posts stuff on the NXT display
Important: use locks to control concurrency between tasks
  Blackboard lock
    Owned by the blackboard task to write the state it updates
    Owned by other tasks when they want to read that state
  Display lock
    Similar

## Slide 29: Tasks: Cautions
RobotC quirk
  A function may be called only by one task at a time
    Exception: all RobotC ‘intrinsics’
  So think carefully about who calls which of the functions you write, and what locks (if any) control that
Avoid ‘deadlock’
  If using multiple locks, define a strict locking order
  E.g.: if you acquire both the blackboard and the display locks, you must get the blackboard lock first
  Exception: leaf locks

## Slide 30: Tasks: Exercise
Write a program that uses the Three Task Architecture
  Choose some sensor(s) for the blackboard task to read if the main task wishes to see them
  Define appropriate stop condition events for those sensors and have the blackboard task compute whether those events have been triggered or not
  Have the main task perform a sequence of actions based on sensor events
    E.g.: Playing beeps or music
    E.g.: Starting or stopping motors
  Have the display task post some useful diagnostic information to the screen
  Bonus: have the blackboard task check for motor stall
    A motor is stalled if it has power applied to it but it hasn’t moved in “a while”